FEATURES OF THE SKETCH - BASE FOR THE FAST PROCESS PLANNING

Predrag Cosic1*, Drazen 2 Antolic

1University of Zagreb, Faculty of Mechanical Engineering and Naval Architecture, Zagreb, Croatia

2 Drazen Antolic (AD) Production Company

*Authors to correspondence should be addressed via email:predrag.cosic@fsb.hr; http://ptp.fsb.hr

Abstract: Very frequently we must answer on  some important requests for offers, generated for individual or batch production, for example : great number of requested offers for production of products at once, small batches with very rarely repetition, frequently changes of priorities during production, short deadlines of delivery, market demands for approaching prices of the individual or batch production near the prices of mass production etc. Purpose of this work is establish possible connections between sketch features and necessary machining times for products manufacturing. Research of the connection between machining time and features of product  can give as result regression equations.

.

Key Words: fast process plannin/, production time/ regression analysis

# 1. introduction

Very frequently we must answer on some important requests for offers, generated for individual or batch production, for example : 1) great number of requested offers for production of products at once, 2) small batches with very rarely repetition, 3) frequently changes of priorities during production, 4) short deadlines of delivery, 5) market demands for approaching prices of the individual or batch production near the prices of mass production etc.

Very important factor for good company competitiveness on the market is technological flexibility.

For successfull company running a business, necessary condition is existence of process planning for every product in saleable process and activities of evaluation of requests of potential customers. It must be stress that often technological knowledge and speed of process planning would be  more important than tehnological level of equipment, skills and knowledge of people who technology realised. So, we can be faced in practice very often by one of two undesirable cases:

.a) great amount of used time for definition process planning of products without agreement of order for production products,

- signing an agreement without estimated  precise machining times/costs necessary for products manufacturing and realization agreed upon products.

# 2. PROCESS PLANNING THROUGH TIMES, COSTS AND DELIVERY

We can find solution in basic technological processes with simple and fast process planning with high level of automatization without works of planners (http://ptp.fsb.hr).

Basic technological process must give requested date to  sales department as the most important date for defining product costs/price and date of delivery. On the other hand, basic tehnological processes can be very useful as the base for detailed process planning or optimization of process planning. We can be faced by few approachs in process planning. For example, definition very precise IF THEN procedure for creation technological knowledge database. Or, we can be faced by use of fuzzy logic and certanities of possible solutions. Or, we can try to solve restricted area of problem by heuristic approach. What can it means?		Technological processes are basicly based upon product sketches with adequately dimensions, tolerancing (dimensional and geometrical), surface roughness, batch size, shape and kind of material, heat treatment, requested delivery, disposable equipment, tools, etc. On the other hand, process plans is primary results of planner experience, intuition and decision support. Very often, process planners work under high level of pressure or lack of time.

Purpose of this work is establish possible connections between sketch features and necessary machining times for products manufacturing. Defined hypopthesis says that established connections we can express, except methods of AI, with equations. Established purpose is to define basic process planning with satisfactory precision.

3. MODEL DEVELOPMENT FOR FORECASTING OF PRODUCTION TIMES

In the near past few approaches for production time’s estimation were developed. For example, estimation of production times & costs by web application for different variants of product production were developed  [1](Figure 1).

# Figure 1 . Selection of machine tools - case for conical machining

Figure 2 Phase - turning of threads with selection shape part, cutting parameters and tim

Selected variant of product production is result of product shape (Figure 2), way of tightening (Figure 1), rough surface and kind of machine tools. Thus, production times and costs are result of observed process planning variant.

Process sequencing based approach [2] (Table 1, Table 2) - the problem that appears next is which  feature should be machined first and more important in which order should features be done. Certainly there are restrictions regarding technology, geometric and dimensional tolerances, datum, economy (reduce production costs and wear or breakage of costly tools). Taking into account all this restrictions is made in which it is clear which features must precede before other features.

| . | execute this operations |
| --- | --- |
| before this operations |  | 2R | 3R | 4R | 5R | 6R | 7R | 8R | 9R | 11R | 12R |
|  | 2R |  |  |  |  |  |  |  |  |  |  |
|  | 3R | X |  |  |  |  |  |  |  |  |  |
|  | 4R |  |  |  |  |  |  |  |  |  |  |
|  | 5R |  |  | X |  | X |  |  |  |  |  |
|  | 6R | X | X |  |  |  |  |  |  |  |  |
|  | 7R |  |  |  |  | X |  |  |  | X | X |
|  | 8R | X |  |  |  |  |  |  |  |  |  |
|  | 9R | X | X |  |  |  |  |  |  |  |  |
|  | 11R |  |  |  |  | X |  |  |  |  | X |
|  | 12R |  |  |  |  | X |  |  |  |  |  |

Table 1. Matrixes of anteriorities for third step

Table 2 Additional criterions for solving conflict situations

In the previous matrixes of anteriorities we have to decide which feature (surface) is going to be machined first 2R or 4R. To make this decision we need more data. In the Figure 3 a few additional criteria were brought out. In order of significance they are:

- same machine tools,

- same process,

- same fixture,

- same tools.

If we look at the Table 2 we can see that feature 1R that proceeded was done by turning process on lathe. Since feature 2R is also done by turning on lathe which means by the same machining process as feature 1R it has advantage before feature 4R. Feature 4R requires milling and therefore different tool and fixture.

Shape complexity approach as the third possible approach for production time’s estimation is defined through entropy as a measure of sample randomness [3].

The entropy is expressed as H=-Σpi.log2pi , where pi is the probability of a certain outcome (angle change along contour in this case). The ultimate goal is to calculate the shape entropy as a measure of shape complexity. Shape shown in Fig. 3 has the entropy of H=2,052.

What can we put as the characteristics for the previous three approaches for possible estimation production times? First, problems with the insufficient generalization level of the used procedure, too complicated calculation, insufficient level of automation of solutions generating in IT application, etc.

Figure 3 Contour of a valve approximated by splines & lines

4. BASIC TECHNOLOGICAL PROCESSES, SKETCH FEATURES AND SEQUENCING OPERATION

Figure 4 Relation between tables (Marks of parts, Realized technological processes -, Elements of realized technological processes and procedure)

Process planning is primarily based on workpiece sketch and requested tolerances (dimensional and geometrical), roughness, heat treatment, material, batch size, planner experience and skills, etc.

So, fundamental idea in fourth approach [4] of production time’s estimation is investigation of existence kind of relationship between shape and date from sketch and process type, process sequencing, primary process, way of tightening, selection of tools, machine tools, etc.

The greatest challenge is to establish (or investigate) the most important factors from sketch for useful, easy, fast and very exact estimation of production times. It is necessary in process of offers definition for better estimation terms of product delivery, production times and costs, manufacturing management and last but not the least important, product price, etc.

As one of the first step in our project research, we have defined possible shapes of raw material and 30 basic technological processes. The fundamental idea is to establish parameters of basic technological processes based on sketch features of considered product.

Parameters of basic technological processes can be:

- shape and kind of raw material (features of sketch, knowledge base),

- type of workpiece (features of sketch, shape and dimensions of raw material),

- necessary operations for treatment (features of sketch, expected production time and knowledge base).

- operations sequencing (features of sketch, , necessary operations of treatment and knowledge base),

- necessary production times (features of sketch based on equations).

So, it have to be establish features of sketch (independent variables), possible dependent variables, size and criteria for sample homogenization (principles of group technology) for analysis of variance and regression analysis.

5. REGRESSION ANALYSIS AS THE BASE FOR THE ESTIMATION MACHINING TIME

Material may be expressed by three basic groupes: quality, shape and dimensions. Investigation of the connection between machining time and features of product (through four group of independent variables) can give as result regression equation. All elements of the sample are records for created datebase (Figure 4.

Considered sample consists of original production documentation one metal manufactured Croatian company. For establishing potential high quality relationship between features of sketch and production time we have to execute two actions.

One action can be explain as exploring measures for reduction number of indenpendent variables for regression analysis. Method of analysis of variance [5, 6] (ANOVA procedure) and stepwise multiple linear regression (MatLab) are helpful in process of reduction of number of indenpendent variables.

The other action was process of sample homogenization (for example, elimination of too big or small value of members of sample).

6. ANALYSIS OF RESULTS

As the precedence work we have to define domain borders of independent variables (less than 40), reduction number of variables by correlation/factor analysis and definition type of smoothing curve with high index of determination. Of course, desired level of generalization in regression analysis would be important indicator for the quality of regression equation. One of the most important problem is process of homogenization of sample of products. Adequate method for this action can be one of methods of group technoogy.

As example of multiple linear regression (four variable) was selected group of rotational parts with heat treatment (Table 3).

Observed multiple linear regression Y = f(X1, X2, X3, X4) has index of determination R2 of 0,969211 (Table 4):

Y = -30.4632 +  0,000489X1 + 7,553821X2 + 0,560182X3 + 124,5732X4

Y = machining time

X1 = workpiece volume

X2 = number of marks for locations and roughness

X3 = number of dimension lines

X4 = requests for locations.

Figure 5 Flow chart

For different group of values of parts (same group) with the significant level of homogenity were established many multiple linear regression equations.

The future research would be conduct in the way of automatic recognition and joining part to the adequate group of parts (logical operators in datebase) .

Research as the second request would include more precise measurement and calculation parts of production times. As the third request would be procedure for estimation multiple linear regression with the least variables, the greatest index of determination and good coincidence calculated and predicted values of dependent variable.

Research work would be continued by looking for adequate model for optimization (minimum of machining time). Implementatioin of the genetic algorithm can be one of possible methods for solving optimization problems.

7. CONCLUSION

Hypothesis about relationship from one side between sketch features and from the other side production times and parameters of technological processes is confirmed. Result of research is fact that possible initial shape of material raw can be automatic defined on the base of the sketch features.

Process of the previous classification parts in defined types of parts based primarily on geometric features is not so important in the process planning. Solution can, indeed, find not in determination type of part but in parts joining to specific, in advance, type of defined fundamental technological processes (OTP) based on sketch features.

ACKNOWLEDGEMENTS

This project is a part of the scientific projects (2007-2009) titled Process Production Impacts to the Competitive and Sustainable Development 120-1521781-3116 financed by the Ministry of Science and Technology of the Republic of Croatia and project supported by Slovenia-Croatia Cooperation in Science and Technology, (2007-2008) named Virtual Manufacturing – Step to Competivity and Sustainable Development financed by the Ministry of Science and Technology of the Republic of Croatia and Slovenian Research Agency (ARSS). We express gratitude for the financial support for the financial support for these projects.

REFERENCES

[] Antolic, D, (2007) Estimation of production times of products by help of regression models, Master thesis would be defended until 30 April 2007., University of Zagreb, Faculty of Mechanical Engineering and Naval Architecture, Zagreb.

[] Balic, J., Veža,I.,  Čuš, F., (2007) Advanced Production Technologies (in Croatian & Slovenian language), FESB, Split & Faculty for Mechanical Engineering, Maribor, 2007, ISBN 86-435-0777-6; Chapter 4. Cosic, P., Process Planning in Web Environment, pp.59-97.

[] Bechhofer, R., E., Santner, T., J.,(1995) Design and Analysis of Experiments for Statistical Selection, Screening, and Multiple Comparisons, John Wiley & Sons, Inc., New York,.

[]BreyfogleIII, F.W., (1992), Statistical Methods, John Wiley & Sons, Inc., New York.

# [] Cosic, P., Levanic, A., (2004), Web Oriented Database System for Pprocess Pplanning, Pacific Congress on Manufacturing and Mmanagement, PCMM) 2004, 8, - 10 December 2004 - Gold Coast, Australia, ISBN 0-9578296-1-2, pp 922-928.

[] http://ptp.fsb.hr/

[] Volarevic, N., Cosic, P., (2005), Improving process planning through sequencing the operations, AMST’05,CISM Courses and Lectures – No. 486 , Springer Verlag, Wien New York, ISBN pp. 337-347.

[] Volarevic, N., Cosic, P. (2005) Shape Complexity Measure Study, DAAAM 2005, Opatija, Croatia, pp 375-376.