ICEIRD2010: Using Multicriteria Optimization in Process Planning

Predrag Cosic1, Dragutin Lisjak2 , Drazen Antolic3

1 Faculty of Mechanical Engenering, Zagreb, Croatia, predrag.cosic@fsb.hr

2 Faculty of Mechanical Engenering, Zagreb, Croatia, dragutin.lisjak@fsb.hr

3AD, Ltd, Ilirski trg 6, Zagreb, Croatia, drazen@adpp.hr

Estimation of production time, delivery term, production costs etc., are some of the key problems of unit production. In the previous research strong correlation was discovered between the features of the product drawing and production time, which has resulted with 8 regression equations. They were realized using stepwise multiple linear regression. Since the optimization of these regression equations did not fully define the most frequent requirements, multicriteria optimization was applied. The applied criteria included: minimum production time, maximum work costs/total costs ratio for a group of workpieces. The group was created using specific classifiers that defined similar workpieces. A STEP model with seven decision variables within a group was applied, and the groups with a high index of determination were selected. Independent values that maximize the work costs/total costs ratio and minimize production times were determined. The obtained regression equations of time production parts and work costs/total costs ratio are included in the objective functions to reduce production time and increasing, work costs/total costs at the same time. The values of decision variables that minimize production time and maximize work costs/total costs ratio were determined. As the solution of the described problem, multicriteria interactive STEP method was applied.

Keywords

multicriteria optimization, STEP method, process planning

1. Introduction

In times of crisis, recession, and in the ‘normal’ business conditions as well, managements are constantly confronted with the same questions: how to reduce production times, delivery, production cycle; how to ‘cut’ all expenses including the costs of product manufacturing, and how to increase own share of the market pie; how to increase productivity; how to balance the productivity of all jobs during the process, especially when cycle production is concerned; how to increase the ratio of productive/unproductive time or cost; how to increase utilization of capacities, how to increase company profits…Such questions are a constant nightmare of all managements of manufacturing companies. Our numerous experiences and experience of others as well, and following of economic trends in Croatia and wider have motivated us to start research in this area. Since a considerable number of research works and papers are dealing with optimization of technological parameters, we have decided to focus our attention on the relationship between product features (geometry, complexity, quantity,..) and production times and costs [1,2,3,4, 5]. It has been proved that it is possible to make estimation of production time applying classification, group technology, stepwise multiple linear regression as the basis for accepting or rejecting of orders, based on 2D [1] drawings, and the set basis for automatic retrieval of features from the background of  3D objects (CAD: Pro/E, CATIA) and their transfer to regression models [4, 5]. Of course, certain constraints have been set: application of standardized production times from technical documentation or estimations made using CAM software (CATIA, PRO/E, CamWorks), type of production equipment/technological documentation determines whether it will be single- or low-batch production. Initial steps have been taken regarding medium-batch, large-batch or mass production. It has been assumed (relying on experience) that small companies (SMEs) in Croatia make decision about acceptance of production (based on customer’s design solution of the product, delivery deadlines and manufacturing costs imposed by the customer - PICOS concept: automotive industry VW, GM) on the basis of free intuitive assessment due to the lack of time and experts. This often results in wrong estimates.

2. Results of regression analysis

One of the authors  was for some time the technical director of INAS company, a successful producer of machine tools in Croatia. Thus, the used technological documentation for conventional machining tools (420 positions) is from that source. By classification of workpieces, determined by BTP form, 8 regression equations for 8 groups of products were obtained. The main grouping criteria were the features (geometrical, tolerance, hardness) from technical drawings and for each workpiece production time was used (technological and auxiliary time).

It was found that the optimization of regression equations, in order to obtain minimum or maximum production times was insufficient with respect to the needs in real production. Thus, the aim was to obtain, by considering a series of regression equations, the optimum for multiobjective optimization (minimal production time, labor cost/material cost ratio or labor cost/total cost ratio for the selected group of products. As multiobjective optimization requires the same variables (x1,...x7), it was necessary to make new grouping of the basic set (302 workpieces) using new classifiers. New classifiers were defined W (1-5), based on 5 basic features:

W1-material: 1(polymers)-5(alloy steel), W2-shape: 1(rotational)-5(complex), W3- max. workpiece dimension: 1(mini V<120mm)-5(V>2000 mm), W4- complexity, BA – number of dimension lines: 1(very simple BA≤5)-5(5 –very complex BA>75), W5- treatment complexity: 1(very rough)-5) very fine). The conditions were defined based on the range of data about the number of dimension lines on the considered sample of 415 elements. A classifier that is being developed is based on 5 basic workpiece features. For the purpose of the research, a group of workpieces (W1-W5) 41113 was selected for further analysis. The code 41113 means: steel – rotational – small – very simple – commonly complex - workpieces. From the available database, the minimum and maximum values for independent variables, and dependent variable (Z1-production time), and derived variable Z2 was taken.

Table 1 Minimum and maximum values of selected variables

| PRODUCT TYPE - 41113 |
| --- |
| min | 2.90 | 0.100 | 1.00 | 11.21 | 0.22 | 0.0132 | 0.001 | 6.00 | 0.92 |
| max | 100.00 | 0.400 | 5.00 | 19.63 | 12.50 | 0.3972 | 0.820 | 33.00 | 1.00 |
| variable | x1 | x2 | x3 | x4 | x5 | x6 | x7 | Z1 | Z2 |
| Variable description | Workpiece outer diameter | Narrowest tolerance of measures | Scale of the drawing | Material mass/strength ratio | Wall thickness/len-gth ratio | Product surface area | Material mass | Production time | Ratio of Work costs/total costs |
| unit of measure | mm | mm | number | number | number | 104 mm2 | kg | h/100 | number |

Two regression equations, Z1 (production time) and Z2 (labor cost/total cost ratio), were selected. For them multiobjective optimization was also performed. In order to use the same types of variables, new grouping was made using specifically adjusted classifiers. Workpiece classification according to the criterion of complexity was done semi-automatically by setting conditions on certain features of drawings (basic roughness, the finest roughness requirement, the narrowest tolerance of measures, the narrowest tolerance of shape or position (geometry), number of all roughness and geometry requirements in the drawing. Each of these 6 criteria based on its specific conditions is assigned a value ranging from 1 to 5. The obtained result is rounded to integer (e.g. 3.49 is W=3, and 3.51 is W=4), and this integer (in the range from  1 to 5) becomes complexity criterion coefficient (the fifth digit in the code).

Table 2 Results of stepwise multiple linear regression

| Regression Statistics | Dependent variable -production time Z1 | Regression Statistics | Dependent variable- work costs/ultimate costs ratio Z2 |
| --- | --- | --- | --- |
| Multiple R | 0.92212166 | Multiple R | 0.99207 |
| R Square | 0.85030835 | R Square | 0.984202 |
| Adjusted R Square | 0.78481826 | Adjusted R Square | 0.977291 |
| Standard Error | 4.09742037 | Standard Error | 0.002725 |
| Observations | 24.0 | Observations | 24.0 |
| Z1 | Coefficients | Z2 | Coefficients |
| Intercept | -13.490042 | Intercept | 0.990439 |
| X Variable 1 | 0.86652065 | X Variable 1 | 0.000238 |
| X Variable 2 | -0.1993556 | X Variable 2 | -0.0039 |
| X Variable 3 | 0.75343156 | X Variable 3 | 0.00046 |
| X Variable 4 | 1.41593567 | X Variable 4 | 0.000794 |
| X Variable 5 | -1.8669075 | X Variable 5 | -0.00107 |
| X Variable 6 | 4.83640676 | X Variable 6 | -0.04466 |
| X Variable 7 | -51.274031 | X Variable 7 | -0.08551 |

3. Description of the model

The general multiciteria optimization problem with n decision variables, m constraints and p objectives is [6]:

(1)

(2)

where is the multiciteria objective function and,,are the p individual objective functions. Benayoun (1971) developed the step method as an iterative technique that should converge to the best-compromise solution in no more than p iterations, where p is the number of objectives. The method is based on a geometric notion of best, i.e., the minimum distance from an ideal solution, with modifications of this criterion derived from a decision maker's (DM) reactions to a generated solution. The method begins with the construction of a payoff table. The table is found by optimizing each of the p objectives individually, where the solution to the kth such individual optimization, called , gives by definition the maximum value for the kth objective, which is called Mk (i.e., Zk(xk) = Mk). The values of the other p - 1 objectives implied by xk are shown in the kth row of the payoff table. The payoff table is used to develop weights on the distance of a solution from the ideal solution. The step method employs the ideal solution, which has components Mk for k = 1, 2, ... , p. The ideal solution is generally infeasible. The , metric is used to measure distance from the ideal solution. The distance is scaled by a weight based on the range of objective Zk and the feasible region is allowed to change at each iteration of the algorithm. The basic problem in the step method is:

(3)

(4)

(5)

where is the feasible region at the ith iteration and  is used to indicate that the original metric has been modified. Initially, ; i.e., at the start of the algorithm the original feasible region is used in (5) The weights in (4) are defined as:

(6)

where

(7)

where nk is the minimum value for the kth objective; i.e. it is the smallest number in the kth column of the payoff table. The  are objective function coefficients, where it is assumed that each objective is linear.

(8)

The solution of (3) to (5) with Fd in (5) yields a non-inferior solution , which is closest, given the modified metric in (6), to the ideal solution. The decision maker (DM) is asked to evaluate this solution. If it is satisfactory, the method terminates; if it is unsatisfactory, then the decision maker specifies an amount ΔZ*k by which objective k* may be decreased in order to improve the level of unsatisfactory objectives, where objective  k* is at a more than satisfactory level. A problem with a new feasible region in decision space is then solved. A solution is feasible to the new problem, x  Fdi+1, if and only if the following three conditions are satisfied:

(9)

(10)

(11)

For the new problem , and the otherare recomputed from (6) for . The problem in (3) to (5) is then resolved with, and since, (7-78) includes constraints for  only. The solution to the new problem yields a new non-inferior solution, which the decision maker evaluates. The method continues until the decision maker is satisfied, which the authors claim occurs in fewer than p iterations.

4. Results of the analysis

On the basis of considerations of regression functions in previous sections, the problem of multiciteria optimization with minimization of the objective functions Z1 and Z2 with related constraints (equations (12) to (14)) is defined.

Min Z1= -13.49004192+0.866520652*x1-0.199355601*x2+0.753431562*x3+1.415935668*x4-

1.866907529*x5+4.836406757*x6-51.27403107*x7	 (12)

Min Z2= -0.990438731-0.000238475*x1+0.003897645*x2-0.00045981*x3-0.000794225*x4+

0.0010738*x5+0.044664232*x6+0.085514412*x7	(13)

x1 ≤ 100; x2 ≤ 0.4; x3 ≤ 5.0; x4 ≤ 19.63; x5 ≤ 12.50; x6 ≤ 0.3972; x7 ≤ 0.820	(14)

x1, x2, x3, x4, x5, x6, x7 ≥ 0

In equations (12) and (13) Z1 represents variable T, and Z2 variable TU/TR. It should be mentioned that for the needs of consistency of the objective functions Z1 and Z2, for the objective function Z2 (equation (13)) the signs of the coefficients of variables and of the free member have been changed. The values of objective functions Z1 and Z2  in the extreme points of the set of possible solutions (feasible region) are given in Table 3. It is visible from the table that that there is no common set of points (x1,... x7) where both functions  Z1 and Z2 have extreme  (maximum) values, and thus the need for optimization of the given problem is justified.

Table 3 Values of the decision variables and the objective functions

| Extreme point | Decision variables | Objective functions |
| --- | --- | --- |
|  | x1 | x2 | x3 | x4 | x5 | x6 | x7 | Z1(x1...x7) | Z2(x1...x7) |
| A | 100 | 0 | 0 | 0 | 0 | 0 | 0 | 73.1620 | -1.0143 |
| B | 0 | 0.4 | 0 | 0 | 0 | 0 | 0 | -13.5698 | -0.9889 |
| C | 0 | 0 | 5 | 0 | 0 | 0 | 0 | -9.7229 | -0.9927 |
| D | 0 | 0 | 0 | 19.63 | 0 | 0 | 0 | 14.3048 | -1.0060 |
| E | 0 | 0 | 0 | 0 | 12.50 | 0 | 0 | -36.8264 | -0.9770 |
| F | 0 | 0 | 0 | 0 | 0 | 0.3972 | 0 | -11.5690 | -0.9727 |
| G | 0 | 0 | 0 | 0 | 0 | 0 | 0.820 | -55.5347 | -0.9203 |

On the basis of the data given in Table 3. the data for the first payoff table (Table 4.) have been selected, which is necessary for the calculation of the first compromise solution,

Table 4 First payoff  table

| Point of optimal solution Xk | Ideal values (Mk) of objective functions (Zk) for Xk |
| --- | --- |
|  | M1=Z1(Xk) | M2=Z2(Xk) |
| X1=(100,0,0,0,0,0,0) | 73.1620 | -1.0143 |
| X2=(0,0,0,0,0,0,0.820) | -55.5347 | -0.9203 |

where k=1...2.  In accordance with equations (6) and (7) coefficients of equation (4) are calculated as follow: α1=0.0197,  α2=10.1974, Π1=0.0019 and  Π2=0.9981.

Arranging the obtained equations, the problem of multiciteria optimization has been practically reduced to the problem of single-objective optimization where the variable  is minimized according to equation (3). The set of equations for the calculation of the first compromise solution of the given problem is shown in Table 5., and the results of decision variables (x1,...x7) and objective functions  Z1 and Z2 are given in Table 6.

Table 5 Set of equations of the first compromise solution

--0.016463892*x1+0.003787756*x2-0.014315200*x3-0.026902778*x4+0.035471243*x5-0.091891728*x6+ 0.974206590*x7 -1.6465 -+0.000238022*x1-0.003890239*x2+0.000458936*x3+0.000792716*x4-0.001071760*x5-0.044579370*x6- 0.085351935*x7-0.070005466 x1 ≤ 100; x2 ≤ 0.4; x3 ≤ 5.0; x4 ≤ 19.63; x5 ≤ 12.50; x6 ≤ 0.3972; x7 ≤ 0.820;

Table 6 Results of the first compromise solution

x1=100; x2=0.4; x3=1.0; x4=12.0428; x5=12.5; x6=0.3962; x7=9999998E-4; =7.128304E-2; Min Z1(x1,...x7) = 69.4161 Min Z2(x1,...x7) = -0.9915 Max Z2(x1,...x7) = 0.9915

Since in the given problem there are two objective functions, it is necessary to make calculation of the second compromise solution, and thus the previous equations for Z1 and Z2 become new constraints shown in equations  (15) and (16)

0.866520652*x1-0.199355601*x2+0.753431562*x3+1.415935668*x4-1.866907529*x5+4.836406757*x6-51.27403107*x7 82.90614192	(15)

-0.000238475*x1+0.003897645*x2-0.00045981*x3-0.000794225*x4 + 0.0010738*x5 + 0.044664232*x6 + 0.085514412*x7   -0.001061269	(16)

Since the value Min Z1(x1,...x7)= 69.4161, it has been decided that the previous value for M1 =73.1620 is to be reduced for the value of 33.1620, and thus the new value for  M1=40. The second  payoff table is given below.

Table 7 Second payoff table

| Point of optimal solution Xk | Ideal values (Mk) of objective functions (Zk) for Xk |
| --- | --- |
|  | M1=Z1(Xk) | M2=Z2(Xk) |
| X1=(100,0,0,0,0,0,0) | 73.1620-33.1620=40 | -1.0143 |
| X2=(0,0,0,0,0,0,0.820) | -55.5347 | -0.9203 |

where k=1...2.  In accordance with equations (6) and (7), coefficients of equation (4) are calculated as follow: α1=0.0199, α2=10.1974, Π1=0.0019 and  Π2=0.9981. Since only the value of variable M1 has been changed, the values of α2 and Π2 remain the same as in the case of calculation of the first compromise solution. As in the case of the first compromise solution, by arranging the obtained equations, the problem of multiciteria optimization has been reduced to the problem of single-objective optimization where the variable  is minimized according to equation (3). The set of equations for the calculation of the second compromise solution of the given problem is shown in Table 8., and the results of decision variables (x1,...x7) and objective functions Z1 and Z2 are given in Table 9.

Table 8 Set of equations of the second compromise solution

--0.001646389*x1+0.000378776*x2-0.001431520*x3-0.002690278*x4+0.003547124*x5-0.009189173*x6+ 0.097420659*x7 -0.101631080 -+0.000238022*x1-0.003890239*x2+0.000458936*x3+0.000792716*x4-0.001071760*x5-0.044579370*x6- 0.085351935*x7 -0.070005466 x1 ≤ 100; x2 ≤ 0.4; x3 ≤ 5.0; x4 ≤ 19.63; x5 ≤ 12.50; x6 ≤ 0.3972; x7 ≤ 0.820; 0.866520652*x1-0.199355601*x2+0.753431562*x3+1.415935668*x4-1.866907529*x5+4.836406757*x6- 51.27403107*x7 82.90614192 -0.000238475*x1+0.003897645*x2-0.00045981*x3-0.000794225*x4+0.0010738*x5 +0.044664232*x6+ 0.085514412*x7 -0.001061269

Table 9 Results of the second compromise solution

x1= 3.37147; x2= 0.3711865; x3= 4.553035; x4= 18.92068; x5= 0.2269908; x6= 0.2826709; x7= 2.965111E-2; = 7.682257E-2; Min Z1(x1,...x7)= 19.0013 Min Z2(x1,...x7)= -0.9915 Max Z2(x1,...x7)= 0.9915

4. Conclusion

The paper presents research on the development of a model for the estimation of production time for unit production or medium size batch production. As a result, eight regression equations were obtained. They show estimation of the production time as a function of geometrical and technological characteristics of a homogeneous group of products that were grouped using logical operators. Using specifically developed 5 classifiers at 5 levels, on the sample taken from the real production a homogenous group was formed which resulted in a regression equation showing dependence between production time (Z1) and 7 independent variables (x1,...x7). After that, the dependence between the work costs/total costs ratio (Z2) and independent variables (x1,...x7) is shown in another regression equation. The optimization part of the work considers the possibility of application of standard STEP method as multiciteria optimization approach in optimization of production problems, where the objective functions are obtained by regression model. The results obtained by application of STEP method indicate that its application is possible in the optimization of decision variables of the given objective functions. It is evident that the results of both objective functions are within the statistical range, i.e. Min Z1(x1,...x7) = 19.0013 and  Max Z2(x1,...x7) = 0.9915, and thus it is not necessary to introduce a new payoff table to find a new compromise (feasible) solution. The following can be concluded: it is cost-effective to manufacture products with minimum outside diameter (x1), maximum (wider range) tolerance (x2), maximum scale (x3), maximum strength/mass ratio (x4), minimum of wall thickness/length ratio (x5), maximum product surface area (x6) and minimum mass of material (x7).

ACKNOWLEDGMENTS

This project is a part of the scientific projects (2007-2009) titled Process Production Impacts  to the Competitive and Sustainable Development 120-1521781-3116 financed by the Ministry of Science and Technology of the Republic of Croatia. We express gratitude for the financial support for these projects.

## References

Antolic, D.: Estimation of production times by regression models (in Croatian language), Master’s thesis, University of Zagreb, Faculty of Mechanical Engineering and Naval Architecture, FSB, Zagreb, 2007.

Volarevic N., Cosic P.Shape Complexity Measure Study, DAAAM 2005, Opatija, Croatia, 2005.

Volarevic N., Cosic P.Improving Process Planning through Sequencing the Operations, 7th International conference on AMST '05(Advanced Manufacturing Systems and Technology), Udine, Italy, 2005.

Kovacic, I.An overview of fast estimation of production times and delivery deadlines (in Croatian), Graduation thesis, University of Zagreb, Faculty of Mechanical Engineering and Naval Architecture FSB, Zagreb, 2007.

Cosic, P, Milcic, D., Kovacic, I. Production Time Estimation as the Part of Collaborative Virtual Manufacturing, International Centre for Innovation and Industrial Logistics -. ICIL  2008, International, March 9 – 15, 2008, Tel Aviv, Israel pp. 93-100.

Cohon, Jared L. Multiobjective programming and planning, Academic Press, Inc. New York , 1978.